To display hidden notes to specifier, from pull down menu “Tools’/”Options”/”View”/”Hidden Text”

Action Bullet Resistant, Inc. – Series # BR/BL-H Model # BR450-8 Door Assemblies

SECTION 083953– BLAST-RESISTANT DOORS

PART 1 – GENERAL

  - SECTION INCLUDES

- Aluminum blast resistant interior and exterior door assemblies in steel frames cladded with aluminum.

  - RELATED DOCUMENTS

- Drawings, and general provisions of the Contract.

  - RELATED SECTIONS

- Section 088853 – Security Glazing

- Section 013300 – Submittal Procedures

- Section 087100 – Door Hardware

  - PERFORMANCE REQUIRMENTS

- Blast Resistant Performance and Design Requirements: Provide security aluminum doors in steel frames cladded with aluminum and the anchorage analysis that comply with requirements indicated and as follows.

  - Blast doors will be calculated to meet: 		Note to specifier: Insert blast level GSA Level D of 10 psi If a greater blast criteria is desired contact a sales representative at Action Bullet Resistant.

  - Blast door will comply with design build blast drawings and calculations.

  - A detailed engineered blast calculations by a qualified blast engineer to substantiate that the system design and anchorage meets or exceeds the minimum performance required.

- Forced Entry Performance and Design Requirements: Provide security aluminum doors in steel frames cladded with aluminum and the design requirements indicated as follows:

- Forced entry doors will meet or exceed the requirements and comply with the testing criteria of ASTM F476-84 Grade 40, forced entry “Standard Test Method for Security of Swinging Door Assemblies”.

- Glazing: Forced Entry requirements of ASTM F1233-98 Class V, forced entry “Standard Test Method for Security Glazing Materials And Systems”

- Impact Protective System and Performance and Design Requirements: Provide security aluminum doors in steel frames cladded with aluminum and the design requirements indicated as follows:

- Impact protective doors will meet or exceed the requirements and comply with the testing criteria of ASTM E 1886-05 standard test method for “Performance of Exterior, Windows, Curtain Walls, Doors and Impact Protective Systems Impacted by Missile(s) and Exposed to Cyclic pressure Differentials” and ASTM E 1996-05b standard specification for “Performance of Exterior Windows, Curtain Walls, Doors and Impact protective Systems Impacted by Windborne Debris in Hurricanes”

- Structural Performance and Design Requirements: Provide security aluminum doors in steel frames cladded with aluminum capable of withstanding wind loads determined as follows, with no permanent deformation or breakage within the assembly when tested according to ASTM E 330-02.

- Air Infiltration and Design Requirements: Provide security aluminum doors in steel frames cladded with aluminum tested under a pressure differential of 6.24 psf when tested according to ASTM E 283-99.

- Water Infiltration and Design Requirements: Provide security aluminum doors in steel frames cladded with aluminum tested under a pressure differential of 8 psf when tested according to ASTM E 331-00.

  - SUBMITTALS

- Design Calculations: Submit design analysis and calculations verifying conformance to specified blast criteria.

- Shop Drawings: Provide elevations indicating rough openings requirements and details for field installed assemblies.

- Qualification Data: Submit qualifications verifying years of experience; include list of completed jobs having similar scope of work, identified by name, location, date contact names and phone numbers.

- Product Data: Provide manufacture’s data sheets on all products used.

- Selection Samples: Provide two product samples for each finish specified.

- Verification Samples: Provide sample for product specified, minimum size 6 inches (150 mm) square, and representing actual product.

  - QUALITY ASSURANCE

- Provide performance test reports from a nationally recognized testing laboratory.

- Drawings and specifications are based on Action Bullet Resistant’s Series BR/BL-H Model BR450-8 single and pair of doors.

- Installer Qualifications: An experienced installer who has completed similar design, material and extent to this project.

- Manufacture’s facility will be made available during production for inspection of doors and windows by customer’s representative to ensure compliance of products with drawings and specifications.

  - DELIVERY, STORAGE AND HANDLING

- Product will be securely crated to prevent damage during shipping. Each crate will be identified by door number and/or elevation. Packing list will identify all contents of crate.

- Verify contents of crate within five days of receipt. If crates are to be stored for log periods due to construction delays, place in a dry warehouse with moderate temperatures.

- When handling crates use forklift or pallet jack.

  - PROJECT CONDITIONS

- Field Measurements: Verify security window openings by field measurements before fabrication and indicate measurements on Shop Drawings.

- Established Dimensions: Where field measurements cannot be made without delaying the work, establish openings and proceed with fabrication without field measurements using held dimensions. Coordinate wall construction to ensure that actual openings dimensions correspond with held dimensions.

  - WARRANTY

- Contractor warrants installation for a period of one year and assumes full responsibility for installation of the system, which includes the window, window system, glass, anchorage, setting, sealing, flashing, etc, as it relates to air, water and structural adequacy as required in the shop drawings and specifications.

- Manufacture warrants products for period of one year from the date of customer receipt.

PART 2 – PRODUCTS

  - MANUFACTURE

- Acceptable Manufacturer: Action Bullet Resistant, Inc., located at 263 Union Blvd. West Islip, NY 11795: Toll Free Tel. 800-962-8088; Tel 631-422-0888; Fax Tel 631-422-4498; Email info@actionbullet.com: Web www.actionbullet.com

  - PRODUCT TYPE

- Security doors and doorframe, pairs of doors with removable mullion.

  - MATERIAL

- Aluminum Extrusions: Aluminum alloy and temper – 6005-T5. Ultimate tensile strength of 37.7 ksi, and shear strength of 29.7 ksi.

- Aluminum Cladding:

- Aluminum Extrusion 6063-T5

- Steel Frame, Mullion and Mullion Retainer Bracket.

- Seamless steel structural tubing 	ASTM A-500.

- Steel plates, shapes and bars 	ASTM A-36

- Silicone: Structural silicone GE SCS 1000 complies with ASTM-C-920-05.

- Glass and Glazing: See Section 088853.

- Setting blocks – Neoprene 80-85 durometer ASTM-D-2000

- Hardware: For custom hardware, contact Action Bullet Resistant’s sales representative for hardware compatibility. Standard door hardware, Select SL11HD continuous mortise hinge Adams Rite 1850 standard keyed cylinder, Rockwood 1” diameter 10” center offset wire push/pull set, Pemko threshold.

  - FABRICATION

- Door is a heavy-duty aluminum medium style. Door thickness 2 15/16” with a 3/8” minimum wall thickness, vertical door stile 4” wide 5 ½” with doorstop, doorframe profile 2” x 6” with a 3/8” minimum wall thickness. Glazing pocket to be 1” deep for proper bite.

- Horizontal top door rail is 5 ½” wide with door stop, additional rails can be added upon request.

Note to specifier: Modify door rail dimension to accommodate additional rails.

- Horizontal bottom rail is 5 ½” wide with a removable stop for glazing in the field, additional rails can be added upon request.

Note to specifier: Modify door rail dimension to accommodate additional rails.

- Doors to have tight hairline joints where rails are fitted against stiles.

- Doorstops snap in as an integral part of doorframe.

- Door accommodates a maximum glass thickness of 2 3/32”

- Doors and frames are fully fabricated and shipped to customer for field installation.

- Fasteners where exposed will be stainless or other non-corrosive material.

- Doors are glazed from the inside by removing the inside steel skin and wet sealed.

- Frames are fully fabricated and shipped to customer for field installation.

- Doorframe 2” x 6” steel rectangular tubing.

  - FINISH

- Exposed surfaces to be free of scratches and other serious blemishes. Anodic finishes are electrolytically deposited Class II finish. Manufactures standard finish:

  - Clear Anodize – 		ASTM-B-137-95

AAMA 608.1

  - Dark Bronze Anodize - 	ASTM-B-137-95

AAMA 608.1

Note to specifier: Delete finish not required.

- Painted Finishes:

  - 770% Kynar-Base	AA-M10-	AAMA 2605

Duranar or Fluropon	C41-RX	ASCA 96

  - Tiger Drylac RAL#

Note to specifier: Delete paint finishes if not required.

# Note to specifier: Insert RAL #

PART 3 – EXECUTION

  - EXAMINATION

- With Installer examine substrates, areas, and conditions for compliance with the requirements for installation tolerances and other conditions affecting functionality and performance of security entrances window systems.

  - Examine rough-in opening for built-in and embedded anchors to verify actual locations of connections before installation.

  - Prepare a written report, endorsed by the installer, listing conditions detrimental to the functionality and performance of security window systems.

  - Examine and inspect built-in and cast-in anchors installations to verify that they comply with requirements. Prepare inspection reports. If removal and replacement is required by inspection, re-inspect after repairs are made and document in inspection report.

  - Clean surfaces thoroughly prior to installation.

  - INSTALLATION

- Door systems shall be installed in their correct locations, set level, square and plumb in alignment with other work and substrates, in accordance with manufactures instructions, approved shop drawings and accepted industry standards. All joints between doors and rough opening shall be sealed using sealant to ensure a weather tight installation.

- Install shall take special care to ensure that impact side of glass faces the threat axis.

- FIELD QUALITY CONTROL

- Inspect installed items to ensure compliance with requirements.

- Protect installed items until completion of project.

END OF SECTION 083953